## Slide 1: Individual Homework
Exercises Boolean functions
Berar denisa- 911

## Slide 2
Exercise 4.1 Boolean Functions
Simplify the following Boolean functions of 4 variables using Veitch diagrams.

## Slide 4: Simplification of Boolean Functions

## Slide 6
= x1 x2 x3 x̄4  x1 x̄2 x3 x̄4  x1 x2 x̄3 x̄4  x1 x̄2 x̄3 x̄4  x1x2 x̄3x4 x̄1 x2 x3x4  x̄1 x2 x̄3x4 
x̄1 x2 x3 x4  x̄1 x̄2 x3 x4 x̄1 x2 x3 x̄4  x̄1 x̄2 x3x̄4  x1 x2 x3 x̄4  x1 x̄2 x3 x̄4  x̄1 x2 x3 x̄4  x̄1 x̄2 x3 x̄4
= m14  m10  m12  m8  m13  m7  m5  m7  m3  m6  m2  m14  m10  m6  m2
=m2  m3  m5  m6  m7  m8  m10  m12  m13  m14

## Slide 8: Factorization process
 | m13 | m5 | m7
m14 | m12 |  | m6
m10 | m8 |  | m2
 |  |  | m3
x1 | x̄1
x3| x̄3 | x3
x4
-----
x̄4
--------
X4
X2
-----
x̄2
Veitch Diagram
- 3 groups of 4 neighbour minterms
- 3 groups of 2 neighbours minterms
=m2  m3  m5  m6  m7  m8  m10  m12  m13  m14

## Slide 9
Double factorization
m7  m6  m2  m3 = x̄1  x3 = max1
Double factorization
m8  m10  m12  m14 = x1  x̄4 = max2
Factorization process
m6  m2  m14  m10 = x3  x̄4 = max3

## Slide 10
Simple factorization
m5  m13 = x2  x̄3  x4 = max4
Simple factorization
m7  m5  m13 = x̄1  x2  x4 = max5
Simple factorization
m12  m13 = x1 x2  x̄3 = max6

## Slide 11
M(f) = {max1, max2, max3, max4, max 5, max6}
C(f) = {max1, max2} = {x̄1  x3 , x1  x̄4}
– the set of central monoms
The minterms coverred by the central monoms are shaded.
We denote g = max1  max2
The simplified form of f:
f1 S(x1x2x3x4) = g  max4
f2 S(x1x2x3x4) = g  max5  max6

## Slide 12: Exercise 4.8 Boolean Functions
m15 |  | m5 | m7
 |  | m4 | 
m10 | m8 | m0 | 
m11 |  | m1 | m3
x1 | x̄1
X2
-----
x̄2
x4
-----
x̄4
--------
X4
x3| x̄3 | x3
= x1 x2 x3 x4  x̄1 x2 x3 x4  x1 x̄2 x3 x4  x̄1 x̄2 x3 x4  x1 x̄2 x3 x̄4  x1 x̄2 x̄3 x̄4  x̄1 x̄2 x̄3 x̄4  x̄1 x2 x̄3 x4  x̄1 x̄2 x̄3 x4  x̄1 x2 x̄3 x̄4  x̄1 x̄2 x̄3 x̄4  x̄1 x2 x3 x4  x̄1 x̄2 x3 x4  x̄1 x2 x̄3 x4  x̄1 x̄2 x̄3 x4
= m15  m7  m11  m3  m10  m8  m0  m5  m1  m4  m0  m7  m3  m5  m1
= m0  m1  m3  m4 m5  7  m8  m11  m15  m10

## Slide 13
Double Factorization:
m3  m7  m11  m15 =x3 x4 = max1
m1  m0  m4  m5 = x̄1 x̄3 = max2
m1  m3 m5  m7 = x̄1 x4 = max3
Simple factorization:
m0  m8 = x̄2x̄3x̄4 = max4
m1  m3 = x̄1 x̄2 x4 = max5
m5  m7 = x̄1 x2 x4 = max6
m10  m11 = x1x̄2x3 =max 7
m10  m8 = x1x̄2x4 = max 8
M(f) = {max1, max2,max3,max4, max5, max6, max7, max8}
Factorization process
- 3 groups of 4 neighbour minterms(max1, max2, max3)
- 5 groups of 2 neighbours minterms(max4, max5, max6, max7,max8)
The set of maximal monoms:
m10

## Slide 14
M(f) = {max1, max2,max3,max4, max 5, max6}
C(f) = {max1, max2, max3} = {x3 x4 , x̄1 x̄3 , x̄2x̄3x̄4 } – the set of central monoms
The minterms coverred by the central monoms are shaded.
We denote g = max1  max2
The simplified form of f:
f1 S(x1x2x3x4) = g  max8
f2 S(x1x2x3x4) = g  max7  max4
m10
m0  m8 = x̄2x̄3x̄4 = max4
m10  m11 = max 7
m10  m8 = max 8