## Slide 1: LOGIC CIRCUITS Exercise 4

## Slide 2: Problem statement
Write a Boolean function of 4 variables given by its table of values, simplify it and draw the logic circuits corresponding to all its simplified forms.

## Slide 7
Basic Gates – IEEE Standards

## Slide 8
Derived Gates: XOR, NAND, NOR, NXOR

## Slide 12
Inputs |  |  |  | Outputs
a | b | c | d | result
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 13: The Veitch Diagram
b | m15 | m13 | m5 | m7 | d
 | m14 | m12 | m4 | m6 | 
 | m10 | m8 | m0 | m2 | 
 | m11 | m9 | m1 | m3 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
used to simplify the results’ formula into DCF

## Slide 14: The Veitch Diagram
b | 1 |  | 1 | 1 | d
 | 1 | 1 | 1 | 1 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d

## Slide 15: I. Double Factorizations
b | 1 |  | 1 | 1 | d
 | 1 | 1 | 1 | 1 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
_
max1 = m11 ∨ m9 ∨ m1 ∨ m3 = bd

## Slide 16
b | 1 |  | 1 | 1 | d
 | 1 | 1 | 1 | 1 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
_
max2 = m5 ∨ m7 ∨ m1 ∨ m3 = ad

## Slide 17: II. Simple Factorization
b | 1 |  | 1 | 1 | d
 | 1 | 1 | 1 | 1 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
max3 = m15 ∨ m7 = bcd

## Slide 18
b | 1 |  | 1 | 1 | d
 | 1 | 1 | 1 | 1 | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
M(result) = {max1, max2, max3}
C(result) = {max1, max2, max3}
M(result) = C(result) => 1st case of the simplifaction algorithm
_ _
The function result(a,b,c,d) = max1 ∨ max2 ∨ max3 = bd ∨ ad ∨ bcd in a disjunctive simplified form

## Slide 19: The Veitch Diagram
b | M15 | M13 | M5 | M7 | d
 | M14 | M12 | M4 | M6 | 
 | M10 | M8 | M0 | M2 | 
 | M11 | M9 | M1 | M3 | d
 | c |  |  | c | 
used to simplify the results’ formula into CCF this time

## Slide 20: The Veitch Diagram
b |  | 0 |  |  | d
 | 0 | 0 | 0 | 0 | 
 | 0 | 0 | 0 | 0 | 
 |  |  |  |  | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d

## Slide 21: I. Triple Factorization
_
max1_d = M14 ∧ M12 ∧ M4 ∧ M6 ∧ M10 ∧ M8 ∧ M0 ∧ M2 = d
b |  | 0 |  |  | d
 | 0 | 0 | 0 | 0 | 
 | 0 | 0 | 0 | 0 | 
 |  |  |  |  | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d

## Slide 22: II. Simple Factorization
_
max2_d = M13 ∧ M12 = a ∨ b ∨ c
b |  | 0 |  |  | d
 | 0 | 0 | 0 | 0 | 
 | 0 | 0 | 0 | 0 | 
 |  |  |  |  | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d

## Slide 23
b |  | 0 |  |  | d
 | 0 | 0 | 0 | 0 | 
 | 0 | 0 | 0 | 0 | 
 |  |  |  |  | d
 | c |  |  | c | 
a
_
a
_
c
_
b
_
d
M_d(result) = {max1_d, max2_d}
C_d(result) = {max1_d, max2_d}
M_d(result) = C_d(result) => 1st case of the simplifaction algorithm
_ _
The function result(a,b,c,d) = max1_d ∧ max2_d = d ∧ ( a ∨ b ∨ c ) in a conjunctive simplified form

## Slide 24: Circuits

## Slide 25
I. Circuit for DCF simplification

## Slide 26
II. Circuit for CCF simplification

## Slide 27: Thanks for your attention!
Ask homework to:
Student 1
Student 2
Student 3
Student 4
Student 5