## Slide 1
Exercise 6.
Using Quine’s method, simplify the following Boolean functions given in DCF (disjunction of minterms):
8. f8(x1,x2,x3)= m0 V m2 V m3 V m4 V m5 V m6
Boolean functions – Simplification using Quine's method

## Slide 2: Steps to follow when applying Quine's method:
1. The initial function f is transformed into DCF(f)
2. Factorization process => the set of maximal monoms M(f)
3. From the set of maximal monoms, the central monoms are selected => C(f)
4. The case of the simplification algorithm is identified and all the simplified forms are obtained

## Slide 3
f8(x1,x2,x3)= m0 V m2 V m3 V m4 V m5 V m6
First, we compute the table containing all the minterms (ordered ascendingly with respect to the number of 1s) with their corresponding binary representation:
-We put a tick mark next to the minterm which appears at least in one mathced pair(or maximal monom).
-A matched pair is obtained when an element form group n differs from an element on group n+1 by only one digit in the binary representation.

## Slide 4
Group | x1 | x2 | x3 | minterm | 
1 | 0 | 0 | 0 | m0 | ✓
2 | 0 | 1 | 0 | m2 | ✓
 | 1 | 0 | 0 | m4 | ✓
3 | 0 | 1 | 1 | m3 | ✓
 | 1 | 0 | 1 | m5 | ✓
 | 1 | 1 | 0 | m6 | ✓
4=1+2 | 0 | _ | 0 | m0Vm2 | ✓
 | _ | 0 | 0 | m0Vm4 | ✓
5=2+3 | 0 | 1 | _ | m2Vm3 =max1 | 
 | _ | 1 | 0 | m2Vm6 | ✓
 | 1 | 0 | _ | m4Vm5= max2 | 
 | 1 | _ | 0 | m4Vm6 | ✓
6=4+5 | _ | _ | 0 | m0Vm2Vm4Vm6=max3 | 

## Slide 5
Max monoms minterms | max1 | max2 | max3
m0 |  |  | *
m2 | * |  | *
m3 | * |  | 
m4 |  | * | *
m5 |  | * | 
m6 |  |  | *

## Slide 6
From the first table, we obtain the following maximal monoms:
max1 =
max2 = x1
max3 =
M(f) = {max1, max2, max3}
After computing the 2nd table, we can conclude that all maximal monoms are central monoms:
C(f) = M(f)=>fS(x1,x2,x3) = max1Vmax2Vmax3 =V