## Slide 1: Cancescu Mihai
Boolean function, Moisil simplification 8.8

## Slide 2: Problem Statement
f(x1,x2,x3)=m0vm3vm4vm6vm7

## Slide 3
Simplifying a Boolean function (given in disjunctive canonical form) means covering all its minterms with a minimum number of maximal monoms and a minimum number of overlaps
Simplification process steps ( steps 2, 3 are specific to Moisil’s method, which is an algebraic simplification method) :
The initial function f is transformed into DCF(f).
The set of maximal monoms are calculated using either one of Veitch-Karnaugh diagrams ( a graphical method) or Quine’s method ( an analytical method). For simplifying f8 we will use Quine’s method.
In order to obtain the simplified forms of the function from the set of maximal monoms, we will use propositional logic.

## Slide 4
Since our initial function (f8 (x1, x2, x3) = m0 v m3 v m4 v m6 v m7 = v v v v ) is already given in DCF, we will jump straight to the factorization process. We will use Quine’s method in order to find the set of maximal monoms M(f).
Sf = {(0, 0, 0), (0, 1, 1), (1, 0, 0), (1, 1, 0), (1, 1, 1)} – the support set of f
The first step of Quine’s method is to order the support set of f with respect to the number of “1” values in each 3-tuple.
Sf = {(0, 0, 0), (1, 0, 0), (1, 1, 0), (0, 1, 1), (1, 1, 1)} (ascending order)
The minterms from the function’s expression are represented using the powers of variables, in a tableau, each minterm on a line, in ascending/ descending order, with respect to the number of “1” values in the 3-tuples of the support of the function. The header of the tableau contains the variables’ names.
Clic pentru a adăuga text

## Slide 5
Sf = {(0, 0, 0), (1, 0, 0), (1, 1, 0), (0, 1, 1), (1, 1, 1)}
I m0
Ii m4
Iii m6
m3
Iv m7
v=i+ii m0vm4= x2x3=max1
vi=ii+iii m4vm6=x1x2=max2
Vii=iii+iv m6vm7=x1x2=max3
m3vm7=x2x3=max4

## Slide 6
The set of maximal monoms obtained:
M(f) = { , , , } = {max1, max2, max3, max4}

## Slide 7
All the minterms from the function’s expression must be covered by a minimum number of maximal monoms, with a minimum number of overlaps. This statement is modelled by the following propositional formula obtained as a conjuction of al previous true sentences:
p1 ˄ (p1 v p2) ˄ (p2 v p3) ˄ p4 ˄ (p3 v p4) ≡ T (CNF with 5 clauses)
This CNF is then transformed into a DNF.
Apply DISTRIBUTIVE laws:
T ≡ (p1 ˄ p1 ˄ p2 ˄ p4) v (p1 ˄ p2 ˄ p2 ˄ p4) v (p1 ˄ p1 ˄ p3 ˄ p4) v (p1 ˄ p2 ˄ p3 ˄ p4)
Apply IDEMPOTENCY:
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) v (p1 ˄ p2 ˄ p3 ˄ p4)
Apply ABSORTION:
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) (DNF with 2 cubes is obtained

## Slide 8
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) (DNF with 2 cubes)
A DNF (disjunction of cubes) is true is at least one of its cubes is true.
For the cube (p1 ˄ p2 ˄ p4) ≡ T:
(x1, x2, x3) = max1 v max2 v max4 = v v
For the cube (p1 ˄ p3 ˄ p4) ≡ T :
(x1, x2, x3) = max1 v max3 v max4 = v v

## Slide 9
Thanks for your attention! :)