## Slide 1: Logic circuits exercise 4
Ciurcău Leonardo-iulian
Group 911

## Slide 2: Logic Circuits Theory

## Slide 3: Basic Gates

## Slide 4: Simplification of Boolean Functions

## Slide 5: Simplification algorithm

## Slide 6: Veitch-Karnaugh Diagram Mehtod

## Slide 7: Exercise 4
m | x1 | x2 | x3 | x4 | f
m0 | 0 | 0 | 0 | 0 | 0
m1 | 0 | 0 | 0 | 1 | 0
m2 | 0 | 0 | 1 | 0 | 0
m3 | 0 | 0 | 1 | 1 | 0
m4 | 0 | 1 | 0 | 0 | 0
m5 | 0 | 1 | 0 | 1 | 0
m6 | 0 | 1 | 1 | 0 | 0
m7 | 0 | 1 | 1 | 1 | 1
m8 | 1 | 0 | 0 | 0 | 0
m9 | 1 | 0 | 0 | 1 | 0
m10 | 1 | 0 | 1 | 0 | 1
m11 | 1 | 0 | 1 | 1 | 1
m12 | 1 | 1 | 0 | 0 | 0
m13 | 1 | 1 | 0 | 1 | 0
m14 | 1 | 1 | 1 | 0 | 1
m15 | 1 | 1 | 1 | 1 | 1
f(x1, x2, x3, x4) = m7 v m10 v m11 v m14 v m15
= x2 x3 x4 v x1 x3 v x1 x3 x4 v x1 x2 x3 v x1 x2 x3 x4

## Slide 8: Veitch diagram

## Slide 9: Simplification of the Boolean function
Set of maximal monoms:
M(f) = {max1, max2}
max1 = m10 v m11 v m14 v m15 = x1 x3 (double factorization)
max2 = m7 v m15 = x2 x3 x4 (simple factorization)
max1 is a central monom because it contains at least a midterm circled only once: m10, m11 and m14
max2 is a central monom because m7 is only circled once
=> all maximal monoms are central monoms => first case of the simplification algorithm
There is a unique simplified form of f, obtained as the disjunction of all central monoms:
= max1 v max2 = x1 x3 v x2 x3 x4

## Slide 10: Conclusion Logic Circuit for f
x1
x3
x1 x3
A
N
D
x2 x3 x4
A
N
D
x2
x4
x1
x3
x2
x3
x4
O
R
f(x1, x2, x3, x4)